## Slide 1: Projet 2013
TaskMain
Synchronize all tasks
TaskSensors
Set or Clear Bumpers flags according to sensors state Execute command from TaskMain
TaskAsser
- Compute new orders to send to motors from current postion to reach expected position
TaskMvt
Compute path necessary to go to expected point. Pre-defined paths are read from « Strategy files » Pre-defined paths are choosen into AppConfig.h file
TaskTime
- Wait 90s and set TIMER_STATUS
QSensors
Queue used to send command from TaskMain to TaskSensor Results are sent by using ACTION_STATUS Flag
App Flags (32 bits) |  |  | 
State 0 - START_BUTTON 1 - 2 - 3 - 4 - 5 - 6 – ACTION_STATUS 7 – TIMER_STATUS | Bumpers (GP2) 8 - GP2_FRONT 9 – GP2_BACK 10 – GP2_HOLDER 11 - 12 - 13 - 14 - 15 - | Bumpers (SW) 16 - 17 - 18 - 19 - 20 - 21 - 22 - 23 - | Not Used 24 – 25 – 26 – 27 – 28 – 29 – 30 – 31 -
StructCmd App_CmdToTaskAsser
StructCmd App_CmdToTaskMvt
TaskOdo
Stand-alone task Compute current position from encoding wheels Postion is exposed by TaskOdo_GetCurrentPos() and TaskOdo_SetCurrentPos()
Strategy Flags (32 bits)
See Page 2

## Slide 2
Strategy Flags (32 bits) |  |  | 
Actions Done 0 - 1 - 2 - 3 - 4 - 5 - 6 - 7 - | Forbbiden Zones 8 - 9 - 10 - 11 - 12 - 13 - 14 - 15 - | Not Used 16 - 17 - 18 - 19 - 20 - 21 - 22 - 23 - | Not Used 24 - 25 - 26 - 27 - 28 - 29 - 30 - 31 -